## Slide 1
PROGRESS REVIEW · CE 766 INTEGRATED DESIGN PROJECT
Prithvi Flood-IN
Pre- & During-Event Inundation Mapping with Prithvi-EO-2.0 over the Indian Subcontinent
INCLINE / LSHMS · AI-Enabled Hydrological Information System for the Mahanadi Basin
Team: Nikhil Upadhyay (Lead) · Prakhar Gupta · Prabhat Kumar · Vineet Jangir · Himanshu Shete
Faculty Supervisor: Prof. Basudev Biswal, Dept. of Civil Engineering, IIT Bombay
Industry Mentor: Vivek Gupta, CTO, ClimMaTech Pvt. Ltd.
23 September 2026
Notes: Introduce the team, supervisor and industry mentor. One line: we adapted a global satellite foundation model to map floods in India, and today we report where we are and what comes next.

## Slide 2
Where we stand today
Fine-tuning is complete; the model now beats the published baseline on unseen Indian floods
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
2
~100
real Indian flood events curated (2021–2026)
3,584
512×512 training chips from 180 image–map pairs
+11%
IoU gain over baseline on held-out test set
+43%
precision gain: far fewer false flood alarms
Completed
Platform walkthrough & literature review
Saint-Venant study + PINN code-base setup
Indian flood dataset built & quality-checked
Evaluation protocol & baseline
Full fine-tune of 300M-param model + before/after evaluation
Inference workflow, applications & Pawna Dam visit
Next
Visual error maps & per-event analysis
Threshold tuning for recall/precision balance
Benchmark against FastFlood; scale up dataset
PINN–SVE training & validation on assigned reaches
Mahanadi-basin pilot & dashboard prototype
Notes: Quick scorecard so the audience knows the headline before the details.

## Slide 3
Project context: INCLINE / LSHMS with ClimMaTech
Our work contributes to product development of the ClimMaTech–IIT Bombay hydrological platform
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
3
The existing platform
A working flood / hydrological modelling software already exists. The brief: understand the code, add parameters, improve the mathematical structure and build a better interface. It also generates automatic LLM-written reports in 16 languages.
Inputs it relies on
Topographic data: river geometry + elevation (DEM).
Rainfall data: observed records for two regions, plus future rainfall to flag flood-prone areas.
Known gaps (kick-off discussion)
• Field surveys of river geometry are costly: ~₹1 lakh for 10–15 km
• River width is observed; depth is computed from equations
• DEM carries about ±1 m vertical error
• Slope comes from a smoothing algorithm, which can be improved
Where our work fits
Objective 1 (agreed with supervisor & mentor): flood inundation mapping with machine learning on satellite imagery (Prithvi Flood-IN). It gives an observed flood extent to validate and enrich the physics-based platform.
Notes: Based on the kick-off meeting (3 Aug) with the supervisor and TA, and the objective statement for the DUGC form.

## Slide 4
Project journey so far
From team formation to a fine-tuned model in about eight weeks
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
4
29 Jul
Team formed; registered for the IDP
3–7 Aug
Kick-off with Prof. Biswal & TA; platform walkthrough; ClimMaTech team joins
12 Aug
Saint-Venant / PINN code base shared: setup + Phase 1
14 Aug
Readings: inundation, routing, runoff generation
26 Aug
Objectives fixed; DUGC proposal submitted
28 Aug
Mentor points us to TerraTorch & Prithvi-EO-2.0 examples
6 Sep
Indian flood fine-tuning catalogue shared for review
10 Sep
FastFlood validation benchmark shared
23 Sep
Fine-tuning complete; progress review
Regular progress reviews with the supervisor, TA and ClimMaTech mentors: 5, 7, 11, 14, 21 and 28 Aug, and 23 Sep.
Notes: Milestones taken from the project group chat.

## Slide 5
Problem & motivation
Why India needs its own flood-mapping model
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
5
Recurring monsoon floods
Monsoon floods recur every year across the Ganga, Brahmaputra and Mahanadi basins, disrupting lives, crops and infrastructure.
Mapping is slow & manual
Official flood maps (NDEM, ISRO/NRSC) are produced by analysts; responders need extents during the event, not days later.
Global models miss India
Prithvi’s flood model was tuned on Sen1Floods11 (non-Indian). Indian terrain, turbid rivers and monsoon clouds shift its behaviour.
Objective
Adapt the Prithvi-EO-2.0 foundation model to Indian flood events so that, given a new Sentinel-2 image, it produces a reliable per-pixel flood-extent map that can feed a hydrological information system for flood response.
Notes: Frame the gap: good global model, but not calibrated for India. Our objective is the India-specific adaptation plus an application pathway.

## Slide 6
Our approach: fine-tune, don’t train from scratch
Transfer learning from an IBM–NASA Earth-observation foundation model
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
6
Prithvi-EO-2.0
Global pre-training
(IBM & NASA)
▶
Sen1Floods11
flood fine-tune
(public checkpoint)
▶
Our India fine-tune
~100 Indian flood events
▶
Prithvi Flood-IN
India-calibrated
flood mapper
Base checkpoint: ibm-nasa-geospatial/Prithvi-EO-2.0-300M-TL-Sen1Floods11 (Hugging Face)
~300 million parameters, Vision Transformer (ViT) encoder: already “understands” land from space
Training from zero would need far more data and compute than a student team has; fine-tuning adapts existing knowledge
Task: semantic segmentation, i.e. a flood / no-flood label for every pixel
Full fine-tune (encoder + decoder unfrozen) using IBM’s open-source TerraTorch library
Notes: Explain the two-stage lineage: general EO model, then flood model, then our India-specific second fine-tune.

## Slide 7
Model architecture
Reused the published Sen1Floods11 architecture and weights, built in TerraTorch
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
7
Input
6-band Sentinel-2 chip
224×224 (train) · 512×512 (eval)
▶
Encoder
Prithvi-EO-2.0 ViT
~300M params (fine-tuned)
▶
Neck
Select layers 5, 11, 17, 23 → tokens to image → feature pyramid
▶
Decoder
UperNet, 256 channels
merges multi-scale features
▶
Head
Per-pixel classifier
[no-flood, flood] · dropout 0.1
Input bands (in order)
B02
Blue
B03
Green
B04
Red
B8A
NIR narrow
B11
SWIR-1
B12
SWIR-2
Shortwave-infrared bands (SWIR-1, SWIR-2) carry the strongest water signal: water absorbs strongly in this part of the spectrum.
Notes: Walk left to right. We did not design a new architecture; we reused the proven one and adapted its weights.

## Slide 8
Building the Indian flood dataset
Sentinel-2 six-band image + NDEM flood map → 512 × 512 training tiles
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
8
221
events in initial flood spreadsheet (only 5 directly usable)
1,022
NDEM flood-extent maps screened (2021–2026)
180
matched image–map pairs across ~100 real flood events
3,584
512×512 chips (2,401 with flood, 1,183 without)
Sources: images from ESA Sentinel-2 (free); ground truth from NDEM (ISRO/NRSC) official flood maps. Pairs rejected when imagery was missing, cloud-covered, or did not overlap the mapped flood.
Notes: Most of the effort went here: finding usable image and flood-map pairs taken during the flood, over the same area, without cloud.

## Slide 9
Data quality & label design
Making sure the model learns the right thing
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
9
Date, event & area matching
Each Sentinel-2 image checked against its NDEM map for same flood event, acquisition during the flood, and geographic overlap.
Cloud masking
Cloud and cloud-shadow pixels set to ignore: we cannot verify what lies underneath, so the model is not trained on a guess.
Permanent water = ignore
NDEM marks only newly flooded land. Rivers and lakes are set to ignore so the model does not learn that “rivers are dry land”.
Clipping & visual QC
Maps clipped to the image footprint: 1.9 GB → 625 MB. Flood outlines overlaid on images and checked by eye.
Label values per pixel
1 Flood
0 Dry land
−1 Ignore: cloud / shadow / permanent water / unmapped
Notes: The ignore label (-1) is the key design decision. Also mention the bug where reflectance scaling had to match the model pre-training normalization.

## Slide 10
Event-wise train / validation / test split
No flood event appears in more than one split, which prevents data leakage
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
10
Split | Events | Images | Chips | Purpose
Train | 72 | 130 | 2,635 | Model learns from these
Validation | 12 | 18 | 212 | Checked every epoch; selects best checkpoint
Test | 16 | 32 | 737 | Held out; used once for final scoring
Why split by event, not by image?
Two images of the same flood look very similar. If one sits in training and the other in testing, the model can score well by recognising the scene rather than understanding floods. Grouping by event makes the test score an honest estimate of performance on a new flood.
Notes: Emphasise rigour: the test set is 16 floods the model has never seen.

## Slide 11
Training configuration & environment
Full fine-tune on free-tier Google Colab (Tesla T4)
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
11
Loss | Cross-entropy, ignore_index = −1
Optimizer | AdamW, LR 5×10⁻⁵, weight decay 0.05
Scheduler | Cosine annealing
Backbone / decoder | Both unfrozen (full fine-tune)
Batch · crop | 8 · random 224×224 crop from 512×512 chip
Precision | 16-bit mixed
Epochs | Max 20; early stop at 15 (patience 8)
Checkpoint | Best val. flood IoU → epoch 7 (0.299)
Environment
GPU: NVIDIA Tesla T4 (15 GB), peak use 7.1 GB
RAM: 12.7 GB (shared VM)
Python 3.13, PyTorch 2.6, TerraTorch 0.99.8, Lightning 2.5, rasterio 1.4
Storage: Google Drive for persistence, local disk for training I/O
Small learning rate on purpose: we are refining a competent model, not training from random weights.
Notes: Early stopping is by design: no epoch after 7 improved validation IoU, so epoch 7 is the final model.

## Slide 12
Engineering challenges we solved
Diagnosed by inspecting the live VM (processes, memory, disk I/O), always resumed from a verified checkpoint
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
12
Library version mismatch
Pre-installed torchaudio clashed with pinned torch → pinned all versions in requirements.txt.
Reflectance scaling
Input values did not match pre-training normalisation, making the model nearly useless → rescaled to expected range.
Validation plotting crash
Default debug plotting needed an interface our dataset lacked → disabled (plot_on_val = False).
Zombie process corrupting checkpoints
After a Colab disconnect a stale process kept writing to Drive → killed it, restored last intact checkpoint, save locally first then sync.
Silent RAM exhaustion
Data-loader workers filled 12 GB RAM and the OS killed training without an error → num_workers = 0 for stability.
Notes: Shows engineering rigour: real failures on free infrastructure, each diagnosed and fixed without losing training progress.

## Slide 13
Evaluation methodology
Same code, same metrics, same 737-chip test set: only the model weights change
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
13
IoU
Overlap ÷ union of predicted and true flood area. Primary metric: cannot be gamed by predicting “no flood” everywhere.
Precision
Of pixels predicted as flood, fraction truly flooded (false-alarm rate).
Recall
Of truly flooded pixels, fraction detected (missed-flood rate).
F1-score
Harmonic mean of precision and recall.
Confusion matrix & inference time
Error breakdown and speed for operational use.
Fair scoring rules
• Scored only on the held-out test set: 16 unseen events, 32 images
• Cloud and permanent-water ignore pixels excluded
• Metrics pooled across all test pixels, plus per-event breakdown
• Visual check: image | NDEM truth | prediction | error map (hits, false alarms, misses)
Notes: Baseline and fine-tuned model evaluated identically so the comparison is apples to apples.

## Slide 14
Results: baseline vs fine-tuned
Held-out test set of 16 unseen Indian flood events
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
14
Chart: 
| IoU | Precision | Recall
Baseline (published) | 0.337 | 0.391 | 0.711
Fine-tuned (ours) | 0.375 | 0.56 | 0.532
Metric | Base | Ours | Δ
IoU | 0.337 | 0.375 | +11%
Precision | 0.391 | 0.560 | +43%
Recall | 0.711 | 0.532 | −25%
Baseline was over-eager: caught most floods, but only 39% of its flood calls were correct
Fine-tuning recalibrated it to Indian conditions: far fewer false alarms
Net effect on IoU, the primary metric, is a clear +11% gain
Precision–recall trade-off is a design choice tied to the end use
Notes: Headline: IoU +11%, precision +43%. Be upfront that recall dropped; early warning may prefer recall, damage assessment prefers precision. Threshold tuning can shift this balance.

## Slide 15
Inference workflow
From a new satellite pass to an actionable flood map
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
15
New Sentinel-2
image
▶
Six-band
pre-processing
▶
Cloud / ignore
masking
▶
Fine-tuned
Prithvi model
▶
Flood-probability
map
▶
Georeferenced
flood-extent map
Overlay layers for decision support
Dams & reservoir releases
Water-level sensors / gauges
Roads & bridges
Villages & population
Critical infrastructure (hospitals, shelters, power)
A new six-band image goes into the trained model, which marks flooded locations and outputs a flood-extent map. Overlaid on roads, villages, dams, sensors and infrastructure, it supports during-event flood-response decisions.
Notes: This is how the model plugs into the hydrological information system envisioned for the Mahanadi basin.

## Slide 16
Where Prithvi Flood-IN can be applied
Application pathways we have researched for the model
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
16
Mahanadi basin HIS
Near-real-time inundation layer for the AI-enabled Hydrological Information System; combine with Hirakud reservoir releases and CWC gauge data.
Disaster response
Flood-extent maps for NDMA / SDMA and district control rooms: evacuation planning, relief routing, identifying cut-off villages and roads.
Agriculture & insurance
Estimate inundated cropland per district to speed crop-loss assessment and insurance claims (e.g. PMFBY).
Infrastructure risk
Flag flooded roads, bridges, substations, hospitals and schools; prioritise restoration.
Hydrological model validation
Observed flood extents to calibrate and validate hydrodynamic / rainfall-runoff model simulations.
Flood-risk planning
Build multi-year inundation frequency maps to support zoning, embankment planning and climate-risk studies.
Notes: Emphasise the Mahanadi HIS link with ClimMaTech, then broader uses. Precision gains matter most for damage assessment and insurance; recall matters most for early warning.

## Slide 17
Physics track: the Saint-Venant equations
1-D shallow-water equations governing unsteady open-channel flow, the basis of flood routing
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
17
Continuity (mass)
∂A/∂t + ∂Q/∂x = q
Momentum
∂Q/∂t + ∂(Q2/A)/∂x + gA ∂h/∂x = gA (S0 − Sf)
Friction (Manning): Sf = n2 Q|Q| / (A2 R4/3)
A | Flow area (m²)
Q | Discharge (m³/s)
h | Water depth (m)
q | Lateral inflow per unit length
S₀ | Bed slope
Sf | Friction slope
n, R | Manning coefficient, hydraulic radius
Simplifications used in practice
Kinematic wave
Friction = gravity; no backwater. Steep rivers.
Diffusive wave
Adds the pressure (depth-gradient) term; captures attenuation.
Dynamic wave
Full equations; needed for tides, dam-break, flat reaches.
Notes: Assigned at the start of the project as a discussion topic. Two equations, mass and momentum, in terms of A and Q. Mention the approximation hierarchy.

## Slide 18
Applications of the Saint-Venant equations
Where the equations are used, and how they connect to our ML flood maps
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
18
Flood routing & forecasting
Propagating an upstream flood hydrograph downstream to predict peak discharge, stage and arrival time.
Dam-break & reservoir release
Simulating release or failure waves below dams; directly relevant to reservoir operations such as those seen at Pawna.
Inundation modelling
1-D/2-D hydrodynamic models (e.g. HEC-RAS, LISFLOOD-FP) predict flood extent and depth on the floodplain.
River engineering
Designing embankments, bridges and channel works for design floods; backwater analysis.
Irrigation & canal operation
Unsteady flow control in canals and gate-scheduling.
Link to Prithvi Flood-IN
Satellite-derived flood extents act as observations to calibrate and validate SVE-based models; the two are complementary.
Notes: Close with the link: physics models predict, satellite ML observes. Together they support a hydrological information system.

## Slide 19
Code basis: physics-informed neural network (PINN) for Saint-Venant
Mentor-provided code base (github.com/Barbhuiya12/PINN), conda env pinn_sve, TensorFlow 1.15 / Python 3.7
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
19
How a PINN solves the SVE
A neural network maps (x, t) → (A, Q) or (h, Q)
Automatic differentiation gives ∂/∂x and ∂/∂t of the outputs
Loss = data misfit (observed gauges / reference solution) + PDE residual of continuity & momentum + boundary / initial conditions
Needs sparse data: physics fills the gaps between gauges
Workflow in the code base
Setup &
verify
Phase 1:
data
exploration
Training
(PINN)
Phase 4:
validation
# PDE residual of the Saint-Venant eqs. (sketch)
def sve_residual(net, x, t):
A, Q = net(tf.concat([x, t], 1))
h = A / B
A_t = tf.gradients(A, t)[0]
Q_t = tf.gradients(Q, t)[0]
Q_x = tf.gradients(Q, x)[0]
F_x = tf.gradients(Q**2 / A, x)[0]
h_x = tf.gradients(h, x)[0]
R = A / (B + 2*h)
Sf = n**2 * Q*tf.abs(Q) / (A**2 * R**(4/3))
r_mass = A_t + Q_x # continuity
r_mom = Q_t + F_x + g*A*h_x - g*A*(S0 - Sf)
return r_mass, r_mom
loss = mse(Q_pred, Q_obs) # gauge data
+ mse(r_mass, 0) + mse(r_mom, 0) # physics
+ mse(bc_pred, bc_obs) # BC / IC
Notes: Six cases = six different river reaches. Phase 1 scripts: p1a_read_reference, p1b_build_training_sets, p1c_explore_plots. Validation target: validate.py --case 3 reports 0.0% deviation. Update status to what the team actually completed.

## Slide 20
Illustrative run: flood-wave routing with the Saint-Venant equations
Our own explicit MacCormack solver on a synthetic 20 km channel (not calibrated to a real river)
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
20
Chart: Time (h)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
x = 0 km (inflow) | 50 | 50.1 | 50.3 | 51.2 | 53.9 | 61.7 | 78.7 | 111.5 | 165.3 | 236.7 | 315.2 | 377.3 | 400 | 375.3 | 312.5 | 234.1 | 162.6 | 109.1 | 77.8 | 60.9 | 53.8 | 51.2 | 50.3 | 50.1 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
x = 8 km | 49.3 | 48.3 | 48.3 | 48.3 | 48.4 | 48.6 | 48.9 | 49.4 | 50.4 | 53.1 | 62.2 | 93.7 | 162.8 | 243.4 | 296.9 | 313.7 | 301.4 | 272.5 | 239.7 | 206.7 | 178.2 | 154.8 | 135.1 | 118.8 | 105.2 | 94.1 | 85.1 | 77.8 | 71.6 | 66.7 | 62.7 | 59.7 | 57.3 | 55.3 | 53.9 | 52.9 | 52.1 | 51.5 | 51.1 | 50.8 | 50.6
x = 20 km | 49.3 | 48.3 | 48.3 | 48.3 | 48.3 | 48.3 | 48.3 | 48.3 | 48.3 | 48.3 | 48.3 | 48.4 | 48.5 | 48.6 | 49 | 50.3 | 58.4 | 98.3 | 157.4 | 201.4 | 223.2 | 229.8 | 227.1 | 218.8 | 207.1 | 194.2 | 180.9 | 168 | 155.3 | 143.5 | 132.3 | 122.5 | 113.4 | 104.9 | 97.4 | 90.8 | 84.8 | 79.6 | 75.1 | 70.9 | 67.4
Location | Peak Q | Peak time
0 km | 400 m³/s | 3.0 h
8 km | 314 m³/s | 3.8 h
20 km | 230 m³/s | 5.3 h
Setup: B = 50 m, S₀ = 0.0005, n = 0.035; base flow 50 m³/s, Gaussian flood peak 400 m³/s
Result: peak attenuates and arrives later downstream (storage + friction)
This is the routing behaviour the PINN learns to reproduce from sparse data
Notes: Python script sve_demo.py (NumPy). Illustrative only; numerical diffusion also contributes some attenuation.

## Slide 21
Field visit: Pawna Dam
Site visit to a monsoon-fed reservoir in Maval, Pune district, Maharashtra
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
21
Why we went
To see how a real reservoir behaves in the monsoon: what our flood maps are meant to support on the ground.
What we observed
Dam structure, spillway and reservoir during the monsoon
How water levels are monitored and releases decided
The link between upstream storage and downstream flood risk
Notes: Describe the visit briefly. Replace the observation bullets with anything specific you discussed on site (gate operation, level gauges, release rules).

## Slide 22
What the dam visit means for our project
Connecting field understanding to Prithvi Flood-IN
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
22
Releases drive floods
Reservoir release decisions during heavy rain shape where and when flooding happens downstream.
Maps + gauges together
Satellite flood extents are most useful when combined with reservoir levels and water-level sensors.
Clouds are real
Heavy monsoon cloud over the reservoir that day showed why optical imagery alone is not enough: motivates SAR fusion.
Impact on our design
Dam and reservoir data are a core overlay layer in our inference dashboard. For the Mahanadi basin, the same idea applies to Hirakud releases combined with CWC gauge readings and our predicted flood extent.
Notes: Tie the visit back to the application: dam data overlay and the need for SAR in cloudy monsoon conditions.

## Slide 23
Limitations
What the current results do and do not show
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
23
Small dataset
~100 events is a meaningful pilot, not production scale. More diverse events (regions, seasons, terrain) are needed.
Optical imagery & clouds
Sentinel-2 cannot see through monsoon cloud, so many during-event scenes are unusable. SAR (Sentinel-1) fusion would help.
Recall dropped
The model now misses more real flood area (recall 0.71 → 0.53). Acceptable for mapping; needs tuning for early warning.
Free-tier compute
Colab disconnects and memory limits constrained experimentation; production runs need stable dedicated compute.
Notes: Stating limitations upfront builds credibility with the mentor and professor.

## Slide 24
Next steps
Plan for the remainder of the project
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
24
1
Qualitative analysis
Error maps (hits / false alarms / misses) and per-event breakdown to find where the model struggles.
2
Recover recall
Tune decision threshold on flood probability; explore class-weighted or Dice loss; report F1.
3
Grow data & benchmark
Screen ~2,680 more NDEM layers; add SAR (Sentinel-1); benchmark against FastFlood validation extents.
4
Mahanadi pilot
Run inference on recent Mahanadi-basin events; validate with ClimMaTech and CWC gauge data.
5
Dashboard prototype
Overlay flood extent with dams, sensors, roads, villages and infrastructure for during-event response.
6
Physics track & final report
Continue PINN–Saint-Venant phases on assigned river reaches; link ML flood extents to the platform; final report & demo.
Notes: Close with a concrete, ordered plan. Invite feedback from the mentor on the preferred precision/recall balance for their use case.

## Slide 25
References
Prithvi Flood-IN | CE 766 Integrated Design Project | Progress Review
25
Szwarcman, D. et al. (2024). Prithvi-EO-2.0: A Versatile Multi-Temporal Foundation Model for Earth Observation Applications. arXiv:2412.02732.
Jakubik, J. et al. (2023). Foundation Models for Generalist Geospatial Artificial Intelligence (Prithvi). arXiv:2310.18660.
Bonafilia, D. et al. (2020). Sen1Floods11: A Georeferenced Dataset to Train and Test Deep Learning Flood Algorithms for Sentinel-1. CVPR Workshops.
Dosovitskiy, A. et al. (2021). An Image is Worth 16×16 Words: Transformers for Image Recognition at Scale. ICLR.
Xiao, T. et al. (2018). Unified Perceptual Parsing for Scene Understanding (UperNet). ECCV.
IBM & NASA. Prithvi-EO-2.0-300M-TL-Sen1Floods11 model card, Hugging Face; TerraTorch library (GitHub).
NDEM, National Database for Emergency Management, NRSC/ISRO: flood inundation layers.
ESA Copernicus Sentinel-2 Level-2A surface reflectance data.
Chow, V.T., Maidment, D.R. & Mays, L.W. (1988). Applied Hydrology. McGraw-Hill (Saint-Venant equations, flood routing).
Raissi, M., Perdikaris, P. & Karniadakis, G.E. (2019). Physics-informed neural networks. J. Computational Physics, 378, 686–707.
Supervisor-shared readings on inundation, flood routing and runoff generation; PINN–SVE code base (github.com/Barbhuiya12/PINN); FastFlood validation (fastflood.org).

## Slide 26
Thank you
Questions & feedback welcome
Nikhil Upadhyay · Prakhar Gupta · Prabhat Kumar · Vineet Jangir · Himanshu Shete
Prof. Basudev Biswal (IIT Bombay) · Vivek Gupta (ClimMaTech Pvt. Ltd.)